## Slide 1
Classroom Presence Verification | Final Review
1 / 8
EMBEDDED SYSTEMS CAPSTONE · FINAL REVIEW
Multi-Node Bluetooth Low Energy (BLE)-Based Classroom Presence Verification System Using ESP32
Kavin J S — CH.SC.U4CSE24119
Lohith Krishnan — CH.SC.U4CSE24153
CSE, Amrita Vishwa Vidyapeetham, Chennai
Notes: Introduce the project: a multi-node BLE presence verification prototype built on two ESP32 nodes and a Flask server. Final review of the implemented and tested system.

## Slide 2
Problem & Objective
Classroom Presence Verification | Final Review
2 / 8
The Problem
Manual attendance is time-consuming and error-prone
Single-node BLE detection can miss devices
Need continuous classroom presence verification
Objective
Use multiple ESP32 BLE nodes for better observation coverage
Detect students who leave during class
Notes: Manual attendance is slow and error-prone, and a single BLE scanner can miss devices. The objective was to use multiple ESP32 nodes for better observation coverage and to detect students who leave during class.

## Slide 3
Final System Architecture
Classroom Presence Verification | Final Review
3 / 8
Student Smartphones
Registered devices advertising BLE names
ESP32 Node 1
BLE scanner
ESP32 Node 2
BLE scanner
Python Flask Server
(Laptop)
Presence Verification
Checks every 10 s using both nodes’ observations
Live Dashboard
Node health, student state
CSV Attendance
Persistent records
BLE
Wi-Fi / HTTP
BLE
Wi-Fi / HTTP
BLE: Smartphone → ESP32
Wi-Fi: ESP32 → Laptop
Nodes send detections and a periodic heartbeat. The system verifies the presence of a registered BLE device, not the identity of a person.
Notes: Registered smartphones advertise over BLE. Two ESP32 nodes scan and send detections plus a periodic heartbeat over Wi-Fi using HTTP to the Flask server on the laptop. The server performs presence verification and feeds the live dashboard and the CSV attendance file.

## Slide 4
Hardware & Software Implementation
Classroom Presence Verification | Final Review
4 / 8
Hardware
2 × ESP32-WROOM-32
Smartphones (nRF Connect advertiser)
LEDs + resistors
Breadboards / jumper wires
Laptop
Software
Arduino IDE + ESP32 framework
BLE scanning
Wi-Fi + HTTP/REST
Python Flask
Rule-based presence logic
Web dashboard
CSV attendance storage
Notes: Hardware: two ESP32-WROOM-32 boards act as BLE scanners, with LEDs and resistors on breadboards. Software: Arduino IDE with the ESP32 framework on the nodes; Python Flask, a web dashboard and CSV storage on the laptop. The verification logic is rule-based.

## Slide 5
Working & Verification Logic
Classroom Presence Verification | Final Review
5 / 8
1
Advertise
Registered phones advertise BLE names
2
Scan
Both ESP32 nodes scan continuously
3
Report
Each detection: name, MAC, RSSI
4
Receive
Server receives detections and heartbeats
In range
≥3 detections from EACH node within a 30 s window
Periodic check
Server re-checks every 10 s throughout the class
Tolerance
A single missed check is tolerated
Left class
No valid evidence for 30 s in a row → considered absent
Final result
PRESENT if ≥75% of counted checks are in range
Node failure
Stale node heartbeat → check skipped, not counted against students
Notes: Data path first: advertise, scan, report, receive. Then the rules: in range means at least 3 detections from each node in a 30 second window; the server re-checks every 10 seconds; 30 seconds of continuous absence means the student left; final result needs at least 75 percent of counted checks in range; a stale node heartbeat skips the check instead of penalising students.

## Slide 6
Implementation Summary
Classroom Presence Verification | Final Review
6 / 8
ESP32 Nodes
Architecture: Slide 3 | Stack: Slide 4
Two nodes scan BLE advertisements continuously
Registered phones detected by both nodes
Report name, MAC, RSSI and a periodic heartbeat
Flask Server
Rules: Slide 5
Combines observations from both nodes
Presence check every 10 s (≥3 detections per node in 30 s)
Stale node heartbeat → check skipped
Outputs
Results: Slide 7
Live dashboard: node health, student state, detection counts, RSSI
Attendance and evidence saved to CSV
RSSI is display-only, not an attendance threshold
Tested: both nodes detect registered devices and attendance is recorded. Test cases and results on Slide 7.
Notes: How the implemented system works end to end: ESP32 nodes scan and report (hardware and software on Slide 4), the Flask server applies the verification rules (Slide 5), and the results appear on the live dashboard and in the CSV file (architecture on Slide 3). Test outcomes are on Slide 7.

## Slide 7
Results & Testing
Classroom Presence Verification | Final Review
7 / 8
Test Case | System Behaviour
Student enters | Detected by both nodes → Present
Temporary missed scan | Not immediately marked absent
Student leaves | Continuous absence detected
Node offline | Attendance checks paused
Both nodes active | Presence verification performed
Recorded attendance results
Kavin — 85.7% → PRESENT
Longest absence 0 s
Kavin — 42.9% → ABSENT
Longest absence 50 s (limit 30 s)
Lohith — 71.4% → ABSENT
Below the 75% threshold
Multi-node observation
Continuous monitoring
Live status visualization
Persistent attendance records
Notes: Left: the tested behaviours. Right: attendance results recorded in the CSV — Kavin 85.7 percent present; Kavin 42.9 percent with a 50 second continuous absence, marked absent; Lohith 71.4 percent, below the 75 percent threshold, marked absent. Bottom: what the tests demonstrate.

## Slide 8
Conclusion & Future Scope
Classroom Presence Verification | Final Review
8 / 8
Conclusion
Successfully implemented a working multi-node BLE presence verification prototype
Combines distributed ESP32 scanning with centralized Flask verification
Supports continuous monitoring and leave detection
Low-cost embedded implementation
Future Scope
More ESP32 nodes for larger classrooms
Better BLE device registration/management
Multi-classroom deployment
Integration with institutional attendance systems
Notes: The prototype is implemented and working: distributed ESP32 scanning with centralized Flask verification, continuous monitoring, leave detection, low cost. Future work: more nodes, better device registration, multi-classroom deployment, integration with institutional systems.